## Slide 1: Evaluating the Efficiency of small Unmanned Aerial Systems (sUas) Against Conventional Field Surveying Techniques for Monitoring Earthen Levee System in South Louisiana
Brennon Dardar¹, Dr. Balaji Ramachandran2, Dr. Gary LaFleur3
1. Geodetic Surveyor, National Geospatial-Intelligence Agency, Holloman AFB, New Mexico
2. Geomatics Department, Nicholls State University, Thibodaux, Louisiana
3. Department of Biological Sciences, Nicholls State University, Thibodaux, Louisiana

## Slide 2: Background
Brennon Dardar
  Former Undergraduate Research Assistant
  Graduate of Nicholls’ Geomatics Program,
  Applied Science
  National Geospatial-Intelligence Agency (NGA)
    Geodetic Surveyor

## Slide 3: Background
Nicholls Geomatics and small Unmanned Aerial Systems (sUAS)
  Working on sUAS technology since 2005
  Coastal Restoration
  Deepwater oil and gas production platform inspection
  Infrastructure monitoring
  Park management
  Surveying
  Agriculture
  Levee monitoring

## Slide 4: Introduction
The Terrebonne Levee and Conservation District's mission is to provide protection by maintaining the integrity of the levee systems and flood control structures.

## Slide 5: Objectives
Compare the accuracy of photogrammetry derived sUAS deliverables against topographic surveying methods
  Differential Leveling
  Real Time Kinematic (RTK) Survey
  Terrestrial Laser Scanning System (TLSS)
  Light Detection and Ranging (LIDAR)
Evaluate the effectiveness of photogrammetry derived sUAS deliverables for monitoring levee structural stability

## Slide 6: Study site
Reach F
  4.5 mile portion of Morganza to the Gulf
  In Dulac, LA
My study’s focus is 200 ft. of levee.

## Slide 7: Methodology
Monument setup at Reach F
Control-GARY
  4 hour GNSS static survey
  National Geodetic Survey (NGS) OPUS solution
LAT(N) | LON(W) | EL HGT
29◦ 20’ 36.31178” | 90◦ 44’ 15.48236” | -23.309 m
Northing (Y) | Easting (X) | ORTHO HGT
93640.713 m | 1057850.618 m | 1.310 m
*REF FRAME: NAD_83(2011) (EPOCH:2010.0000)
*State Plane Coordinates ( Zone 1702 Louisiana South)

## Slide 8: Methodology
Nails placed at a 20ft. (6.096 m.) stations along the levee alignment.
  Nails placed at each station included variations in grade (crown, toe shoulder etc.)

## Slide 9: Methodology
Differential Leveling
  Nikon AC-2s Automatic Level and Crain Level Staff/Rod
  20ft. interval cross sections.
    Points at each station included changes in grade (crown, toe shoulder etc.)

## Slide 10: Methodology
Real Time Kinematic (RTK) GNSS Survey
  Trimble R10 GNSS Receivers (Base and Rover), and Pacific Crest ADL Vantage Pro Radio Unit
  20ft. interval cross sections
    Same location as differential leveling points

## Slide 11: Methodology
Terrestrial Laser Scanning System (TLSS)
  Trimble VX Spatial Station
    1 to 250 meter range; up to 15 points/sec, typically 5 points/sec; 10mm minimum point spacing

## Slide 12: Methodology
Photo Derived Small Unmanned Aerial System (sUAS)
  Trimble UX5HP (Delair), Sony Alpha a7R prosumer camera with 35mm wide-angle lens, and Kestrel 4500 Pocket Weather Tracker
    Fixed wing sUAS

## Slide 13: Methodology
Light Detection and Ranging (LIDAR)
  Active Sensor
  RIEGL VUX-1 UAV
    10 mm survey-grade accuracy
    500,000 measurements / second
    Up to 330˚ field of view
    Lightweight (3.5 kg) and rugged unit

## Slide 14: Methodology
Data processing software:
  Trimble Business Center (TBC) 4.0
    All data surfaces were created within TBC to be compared using the same TIN surface algorithm.
Photogrammetry derived 3D point cloud
TIN surface derived from above 3D point cloud

## Slide 15: results
Differential Leveling
Sections | Number of Points | Time (min.) | Volume (m3)
6.096 m (20 ft.) | 77 | 82 | 2332.0
12.192 m (40 ft.) | 42 | 45 | 2337.9
30.480 m (100 ft.) | 21 | 23 | 2337.7
RTK Survey
Sections | Number of Points | Time (min.) | Volume (m3)
6.096 m (20 ft.) | 77 | 60 | 2322.9
12.192 m (40 ft.) | 42 | 38 | 2326.4
30.480 m (100 ft.) | 21 | 24 | 2315.3

## Slide 16: results
Diff. Leveling v/s RTK
Legend | 
Surface | Color
Conventional Differential Leveling | 
RTK GNSS Survey | 

## Slide 17: results
Differential Leveling
TLSS
Sections | Number of Points | Time (min.) | Volume (m3)
6.096 m (20 ft.) | 77 | 82 | 2332.0
12.192 m (40 ft.) | 42 | 45 | 2337.9
30.480 m (100 ft.) | 21 | 23 | 2337.7
Number of Scans | Number of Points | Time (min.) | Volume (m3)
16 | 101621 | 565 | 2494.8
Difference

## Slide 18: Results
Legend | 
Surface | Color
Conventional Differential Leveling | 
RTK GNSS Survey | 
TLSS | 
LIDAR | 
Photogrammetry Derived | 

## Slide 19: Results
Volume excess measured from TLSS surface model = 162.8 m3
Surface area = 898.1 m2
Avg. grass height = 17.78 cm
Estimated volume excess due to noise (grass) = 159.7 m3
Volume difference RTK v/s Photogrammetry = 38.2 m3

## Slide 20: Results
Legend | 
Surface | Color
Conventional Differential Leveling | 
LIDAR | 
Photogrammetry Derived | 
Diff. Leveling, LIDAR, and Photo Derived

## Slide 21: Results
sUAS
  Setup time for GNSS base station: 10 min.
  Setup time for 34 photo controls: 60 min.
  Flight mission related time: 53 min.
  Processing time: 18 hours.
    Dell Precision Workstation, Intel Xeon 2.4 GHz Dual Processor, 64.0 GB RAM, 64 bit Windows 7 Professional Operating System

## Slide 22: Results
Check Point | East (ΔX) m | North (ΔY) m | Elevation (ΔZ) m
Mean | 0.0113 | -0.0016 | -0.0019
Stand Dev | 0.0075 | 0.0064 | 0.0012
RMSE | 0.0132 | 0.0062 | 0.0022
RMSEr | 0.0146 |  | 
Hor. Accuracy | 0.025 | @ 95% Confidence Level | 
Vert. Accuracy | 0.004 | @ 95% Confidence Level | 

## Slide 23: Results
Number of Flights | Number of Points | Time (min.) | Volume (m3)
1 | 67,226,871 | 123 | 2353.5
Difference Between Differential Leveling and Photogrammetry Derived sUAS deliverables

## Slide 24: Results
Number of Flights | Number of Points | Time (min.) | Volume (m3)
1 | 34,969,416 | 100 | 2379.8
Difference Between Differential Leveling and LIDAR

## Slide 25: results
TLSS, Photo Derived, and LIDAR Cross Sections
All surface model profiles follow the same trend but shift due to noise.
Legend | 
Surface | Color
TLSS | 
LIDAR | 
Photogrammetry Derived | 

## Slide 26: Conclusions
Differential Leveling to RTK 9.1 m3 = 11.9 yd3
Diff. Leveling to Photo Derived 21.5 m3 = 28.21 yd3
In other words over 200 ft., the volume estimation is off by almost 2 small truck loads.
  Over 4.5 miles the volume estimates would be off by 238 loads.
sUAS orthomosaics will be a valuable topographic map.
sUAS proves to be well suited as a levee monitoring tool by providing accurate volumetric estimates compared to other topographic surveying methods.

## Slide 27: acknowledgements
This study was funded by Terrebonne
Parish Consolidated Government (TPCG)
grant.
I would like to thank the following individuals:
  Mr. George Rey, Mr. Peter Jensen, Mr. Mert Pellegrin, Mr. Cody Parks, Mr. Terry Parks, Mr. Lee Drennan, and Mr. Amir Izadi
I would also like to thank Chustz Surveying LLC. and Terrebonne Levee and Conservation District.

## Slide 28: Questions?
Thank you
Contact Information:
  Brennon Dardar
  Geodetic Surveyor
  National Geospatial-Intelligence Agency
  Graduate of Nicholls’ Geomatics Program, Applied Science
  E-mail: bdardar1@nicholls.edu
  Dr. Balaji’s contact Phone: (985) 448-4724